Poster session Abstract no. E73

STORAGE OF SLURRY IN EARTH-BANKED LINED BASINS IN FINLAND

Maarit Hellstedt* and Teemu AlaKleme, *MTT Agrifood Research Finland, Animal Production

Research, Kampusranta 9 C, FI-60320 Seinäjoki, Finland; maarit.hellstedt@mtt.fi

Earth-banked basins are commonly applied in many countries to store slurry. Their design varies

from simple ponds without any provisions to well monitored storage facilities with thick plastic

sheets, protecting the soil underneath. In Finland there have occurred breakdowns of earthen

manure stores. These failures have led to demands for slapping a band for this kind of slurry

storages. The situation is uncomfortable because according to BAT-documents a lagoon is equally

viable as a slurry tank, providing it has impermeable base and walls in combination with leakage

detection and provisions for a cover. This research project consists of two different parts. In the first

part information and literature of the use and regulations of this kind of slurry storages in different

European countries was gathered up. The second part of the project was visits on four farms having

earthen lined slurry storages. From there the plans for construction work were checked and the

condition of the earthen storages was inspected. From the results of the farm visits made and from

the instructions and other material got from the companies selling lining materials for lagoons it was

concluded that from the point of view of material technology the earthen lined storages are

acceptable. The farm visits pointed out the significance of the careful construction work and of the

use of suitable machinery both in construction and operation of a lagoon. In the literature and

instructions the importance of site investigations (such as geological report, ground survey, soil

investigation, determining the depth to bedrock and the depth to the seasonable high water table)

are out lined. Also the importance of professional doers is emphasized. When comparing the Finnish

guidelines and the results of farm visits to the literature and instructions from other countries certain

additions to our guidelines are worth to consider.

218

24th NJF Congress and 2nd NFS Conference 2011